## Slide 1: Lecture 10 Computer Architecture and Basic Performance
Dr. Brendan Kochunas
10/07/2018
NERS 590-004

## Slide 2: Outline
Motivating example:
  Lab 4 Matrix-matrix Multiply
Basic notions of serial performance
Computer Architecture
  How do we understand it?
  Memory Hierarchy
  How to characterize the “micro-architecture”
  Things that happen in parallel and parallel architectures

## Slide 3: Learning Objectives
Insights into Lab 4
Understand the definition of performance.
Understand what parts of computer hardware affect performance.
Understand detailed practical models for architecture of processors and supercomputers

## Slide 4: Motivation

## Slide 5: Matrix-matrix Multiply
Lab 4
  Write your own matrix-matrix multiply
  Compare to dgemm from BLAS
    For system BLAS library and OpenBLAS
    Compare to NumPy

## Slide 6: Results for Lab 4
Results obtained on Great Lakes
Matrix Size | My Implementations |  |  | System BLAS | OpenBLAS | NumPy | MKL
100 | 0.001 | 0.001 | 0.003 | 0.001 | 0.064 | 0.002 | 0.002
500 | 0.062 | 0.068 | 0.465 | 0.071 | 0.069 | 0.007 | 0.007
1000 | 0.505 | 0.559 | 4.109 | 0.575 | 0.291 | 0.034 | 0.034
2000 | 5.516 | 6.160 | 39.028 | 5.787 | 0.749 | 0.231 | 0.231
4000 | 47.922 | 50.341 | >100 | 46.229 | 2.822 | 1.690 | 1.682
Clearly something is going on here...
Notes: $ python >>> import numpy >>> numpy.__config__.show()

## Slide 7: Matrix-matrix Multiply
Lab 4
  Write your own matrix-matrix multiply
  Compare to dgemm from BLAS
    For system BLAS library and OpenBLAS
    Compare to NumPy
do i=1,n
do j=1,n
do k=1,n
c(i,j)=c(i,j)+a(i,k)*b(k,j)
enddo
enddo
enddo
c=MATMUL(A,B)
Fortran one-liner
do k=1,n
do j=1,n
do i=1,n
c(i,j)=c(i,j)+a(i,k)*b(k,j)
enddo
enddo
enddo

## Slide 8: NumPy uses MKL!
Turns out...
  NumPy uses Intel MKL!
Anaconda (and probably Canopy) distributions of NumPy also include Intel MKL libraries!
MKL has a free community edition library.
$ python >>> import numpy >>> numpy.__config__.show()
lapack_opt_info:
libraries = ['mkl_intel_lp64', 'mkl_intel_thread', 'mkl_core', 'iomp5', 'pthread']
library_dirs = ['/sw/lsa/centos7/python-anaconda2/created-20170424/lib']
define_macros = [('SCIPY_MKL_H', None), ('HAVE_CBLAS', None)]
include_dirs = ['/sw/lsa/centos7/python-anaconda2/created-20170424/include']
blas_opt_info:
libraries = ['mkl_intel_lp64', 'mkl_intel_thread', 'mkl_core', 'iomp5', 'pthread']
library_dirs = ['/sw/lsa/centos7/python-anaconda2/created-20170424/lib']
define_macros = [('SCIPY_MKL_H', None), ('HAVE_CBLAS', None)]
include_dirs = ['/sw/lsa/centos7/python-anaconda2/created-20170424/include']
openblas_lapack_info:
NOT AVAILABLE
lapack_mkl_info:
libraries = ['mkl_intel_lp64', 'mkl_intel_thread', 'mkl_core', 'iomp5', 'pthread']
library_dirs = ['/sw/lsa/centos7/python-anaconda2/created-20170424/lib']
define_macros = [('SCIPY_MKL_H', None), ('HAVE_CBLAS', None)]
include_dirs = ['/sw/lsa/centos7/python-anaconda2/created-20170424/include']
blas_mkl_info:
libraries = ['mkl_intel_lp64', 'mkl_intel_thread', 'mkl_core', 'iomp5', 'pthread']
library_dirs = ['/sw/lsa/centos7/python-anaconda2/created-20170424/lib']
define_macros = [('SCIPY_MKL_H', None), ('HAVE_CBLAS', None)]
include_dirs = ['/sw/lsa/centos7/python-anaconda2/created-20170424/include']

## Slide 9: Performance Basics
To understand the performance you observe, you first have to understand what performance to expect
To have an expectation of performance, we all have to be on the same page about what performance is

## Slide 10: What is performance?
What does it mean for a code to be fast?
The real metric: Time
Derived metrics
  FLOPS = FLoating Point OPerations per Second
  Bandwidth = data per unit time (sort of like a flow rate)
  Latency = Minimum time for data to travel from point A to point B
Theoretical Peak Performance
  Very difficult to achieve in practice
  Can be computed from hardware specs
Do things efficiently in time
How do you get fast code?
First: Choose the right algorithm
Second: Understand how to express that algorithm in the programming language
Third: Understand how the source code will get mapped to the hardware
Fourth: Tune the code to the hardware
A lot of this can be done with pen and paper

## Slide 11: Computer Architecture

## Slide 12: Idealized Processor Model
Processor names bytes, words, etc. in its address space
  These represent integers, floats, pointers, arrays, etc.
Operations include
  Read and write into very fast memory called registers
  Arithmetic and other logical operations on register
Order specified by program
  Read and returns the most recently written data
  Compiler and architecture translate high level expressions into “obvious” Lower level instructions
  Hardware executes instructions in order specified by compiler
Idealized Cost
  Each operation has roughly the same cost (read, write, add, multiply, etc.)
A+B=C
Read address(A) into R1
Read address(B) into R2
R3 = R1 + R2
Write R3 to address(C)
Floating Point Math
Integer Math
Memory
Processor
Registers

## Slide 13: Real World Processors
Intel “Nehalem”
AMD “Bulldozer”
Notes: Intel Figure: By I, Appaloosa, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=2541872
AMD Figure: By Shigeru23 - Made by uploader (ref:[1], [2], [3]), CC BY 3.0, https://commons.wikimedia.org/w/index.php?curid=17130259

## Slide 14: “Single” Processor Concept
Real world processors have
  Registers and caches
    Small amounts of fast memory
    Stores values of recently used data nearby
    Different memory operations can have very different costs
  Parallelism
    Multiple “functional units” that can run in parallel
  Pipelining
    A form of parallelism like assembly line
Why is this your problem?
  In theory, compilers and hardware “understand” all this complexity
  and can optimize our programs; in practice they do not often do this well
  Compilers do not know about different algorithms that might be better
We want to know the details to use processors effectively
  Don’t want to know all the details
  Don’t want to have an incomplete model.
FPU
ALU
Processor
Data Cache
Instr. Cache
L2 Cache
Main Memory
… levels of cache
Registers

## Slide 15: Cache Basics
Cache is fast (expensive) memory which keeps copy of data in main memory;
  Typically it is hidden from software (e.g. no standard way of programming directly)
  Simplest example: data at memory address xxxxx1101 is stored at cache location 1101
Cache hit: in-cache memory access—cheap
Cache miss: non-cached memory access—expensive
  Need to access next, slower level of cache
Cache line length: # of bytes loaded together in one entry
  Ex: If either xxxxx1100 or xxxxx1101 is loaded, both are
Associativity
  direct-mapped: only 1 address (line) in a given range in cache
    Data stored at address xxxxx1101 stored at cache location 1101, in 16 word cache
  n-way: n ≥ 2 lines with different addresses can be stored
    Up to n ≤ 16 words with addresses xxxxx1101 can be stored at cache location 1101 (so cache can store 16n words)

## Slide 16: Why have multiple levels of cache/memory?
Most programs have a high degree of locality in their memory access patterns
  Spatial locatility: accessing data nearby previously accessed data
  Temporal Locality: access data and reuse that data a lot
  A memory hierarchy attempts to exploit locality to improve overall average access time.
Cache is small and fast (speed = $$$)
  A large cache always has delays: time to check addresses is longer
  There are other parts to memory hierarchy (TLB, pages, swap, etc.)
Attempts to reconcile Processor/Memory Gap

## Slide 17: Processor-DRAM Gap (latency)
Slide Source: Jim Demmel
Main delay is mostly communication time
Memory is getting bigger (increases access times)
Notes: Y-axis is performance
X-axis is time
Latency
Cliché:
Not e that x86 didn’t have cache on chip until 1989

## Slide 18: Memory Hierarchy
 | Register | L1 | L2 | L3 | DRAM | Disk | Tape
Size | < 1 KB | ~1KB | 1 MB | 10’s MB | 1-100’s GB | TB | PB
Speed | < 1ns | <1 ns | ~1 ns | ~1-10 ns | 10-100 ns | 10 ms | ~10s
L1 cache
L2 and L3 cache
(SRAM)
Main Memory
(DRAM)
Disk
On chip
Tape Archival Storage

## Slide 19: Techniques for exposing details of Memory
Determine memory access times experimentally using “micro”-benchmarks
  Membench (Saavedra-Barrera), STREAM, others…
time the following loop
(repeat many times and average)
for i from 0 to L
load A[i] from memory (4 Bytes)
for array A of length L from 4KB to 8MB by 2x
for stride s from 4 Bytes (1 word) to L/2 by 2x
time the following loop
(repeat many times and average)
for i from 0 to L by s
load A[i] from memory (4 Bytes)
s
1 experiment

## Slide 20: Membench: What to Expect
Consider the average cost per load
  Plot one line for each array length: time vs. stride
  If array is smaller than a given cache all accesses will hit (after first run)
  Small stride is best: e.g. if cache line holds 4 words, expect ¼ miss
  Picture assumes one-level cache
  More difficult to measure on modern processors due to more complex memory systems
s = stride
average cost per access
total size < L1
cache hit time
memory
time
size > L1

## Slide 21
L1:
16 KB
2 cycles (6ns)
Example Membench Results
for
Sun Ultra-2i, 333 MHz
L2: 64 byte line
See www.cs.berkeley.edu/~yelick/arvindk/t3d-isca95.ps for details
L2: 2 MB,
12 cycles (36 ns)
Mem: 396 ns
(132 cycles)
8 K pages, 32 TLB entries
L1: 16 B line
Array length
Notes: Each symbol is an experiment, vertical axis is time/load
Experiments with same length array share symbol, color, joined by line
Such experiments differ only in stride in bytes (horizontal axis)
note that minimum stride = 4 bytes = 1 word
4) Main Observation 1: complicated, depending on array length and stride
5) Main Observation 2: time/load ranges from 6 ns to 396 ns, 66x difference – important!
6) Detail 1: bottom 3 lines (4KB to 16KB) take 6 ns = 2 cycles, but 32KB and larger take longer
deduce that L1 cache is 16 KB, takes 2 cycles/word (yes, according to hardware manual)
7) Detail 2: next 6 lines (32 KB to 1MB) take 36ns = 12 cycles for small stride (2MB a little more)
but 4MB takes much longer:
deduce that L2 cache is 2MB, takes 12 cycles/word (yes)
8) Detail 3: remaining lines take 396 ns = 132 cycles for medium stride,
deduce that main memory takes 132 cycles/word
9) Detail 4: look at 32KB to 1MB lines, speed halves from stride 4 to 8 to 16, then constant
deduce that L1 line size is 16 bytes
10) Detail 5: look at 4MB to 64MB lines, speed halves from stride 4 to 8 to … to 64, then constant
deduce that L2 line size is 64 bytes
11) Detail 6: look at lines 32KB-256KB, vs 512 KB-2MB, increase up to 8KB stride of latter
deduce that page size is 8 KB, and TLB has 256KB/8KB = 32 entries

## Slide 22: STREAM Benchmark
STREAM: Sustainable Memory Bandwidth in High Performance Computers
  Measures sustainable memory bandwidth (in MB/s) based on simple vector kernels
  Developed & maintained by Dr. John D. McCalpin at University of Virginia
Developing “second-generation” STREAM benchmark (STREAM2)
  Emphasis is on measuring
    Bandwidth of memory hierarchy, latency, other access patterns, locality (e.g. bandwidth and latency between distributed shared memory systems)
    https://www.cs.virginia.edu/stream/ref.html
------------------------------------------------------------------
name kernel bytes/iter FLOPS/iter
------------------------------------------------------------------
COPY: a(i) = b(i) 16 0
SCALE: a(i) = q*b(i) 16 1
SUM: a(i) = b(i) + c(i) 24 1
TRIAD: a(i) = b(i) + q*c(i) 24 2
------------------------------------------------------------------

## Slide 23: Single Core Parallelism
Pipelining
  Like an assembly line, have different parts of processor doing things in parallel
  Just know that this happens, you don’t have much ability to control this, other than perhaps some compiler options
Vector Instructions (SIMD)
  SIMD = Single Instruction Multiple Data
  As a programmer, you have some control over this…
    Use of compiler options
    Also have to write your code in a way that lets compiler recognize SIMD
    Easily expressible in Fortran with intrinsic array operators and functions

## Slide 24: Pipelining
In this example:
  Sequential execution takes 4 * 90min = 6 hours
  Pipelined execution takes 30+4*40+20 = 3.5 hours
Bandwidth = loads/hour
BW = 4/6 l/h w/o pipelining
BW = 4/3.5 l/h w pipelining
BW <= 1.5 l/h w pipelining, more total loads
Pipelining helps bandwidth but not latency (90 min)
Bandwidth limited by slowest pipeline stage
Potential speedup = Number pipe stages
A
B
C
D
6 PM
7
8
9
T
a
s
k
O
r
d
e
r
Time
30
40
40
40
40
20
Dave Patterson’s Laundry example: 4 people doing laundry
wash (30 min) + dry (40 min) + fold (20 min) = 90 min
Latency

## Slide 25: Single Instruction Multiple Data
One operation produces multiple results
Implemented as SSE assembly instructions by compiler
  SSE = Streaming SIMD Instructions
  Several standards SSE (128-bit), SSE2, … SSE4, AVX (256-bit), AVX2 (512-bit)
Operate on anything that fits into x bytes (e.g. 16 bytes)
  Operations include add, multiply, etc.
Challenges
  Need to be contiguous in memory and aligned
  Some instructions are needed to move data around from one register to another
128-bit
64-bit
256-bit
x0
x1
x2
x3
y0
y1
y2
y3
x0+y0
x1+y1
x2+y2
x3+y3
+
=
256-bit wide vector

## Slide 26: Cores, Processors, and Nodes OH MY!
We have been narrowly focused on a “single core”.
  Many processors are “multi-core”
  Common for motherboards to have multiple “sockets” or processors
  A node has one motherboard, with multiple processors, and each processor has multiple cores
Other terminology
  Symmetric Multi-processor (SMP)
  Non-Uniform Memory Access (NUMA)
Illustration of Titan Compute Node [1]
[1] - https://www.olcf.ornl.gov/support/system-user-guides/titan-user-guide/

## Slide 27
Flux node (generated by lstopo)

## Slide 28: Contemporary HPC Platforms
Scratch Space
(Lustre File system)
Project
Home
Archival
Storage
I/O Server
Login1
Login2
…
…
Data Transfer Nodes
Compute Nodes
Job Server
Metadata Servers
Users

## Slide 29: Memory Hierarchy for Distributed Machines
Node
 | Register | L1 | L2 | L3 | DRAM | Cluster | Disk | Tape
Size | < 1 KB | ~1KB | 1 MB | 10’s MB | 1-100’s GB | TB | TB | PB
Speed | < 1ns | <1 ns | ~1 ns | 1-10 ns | 20-100ns | 1-100 μs | 10 ms | ~10s
L1 cache
L2 and L3 cache
(SRAM)
Main Memory
(DRAM)
Disk
On chip
Tape Archival Storage