## Slide 1: Lecture 11 Serial Performance and Optimization
Prof. Brendan Kochunas
10/09/2019
NERS 590-004

## Slide 2: Outline
Motivation
Defining Performance
Performance Analysis of Matrix-Vector Multiply
Common techniques for serial optimization
More advanced optimizations

## Slide 3: Learning Objectives
Understand what computational intensity is
Understand how to construct and utilize a performance model
Understand tricks for optimizing code

## Slide 4: Motivation and Defining Performance

## Slide 5: Motivation for Performance
We can run more simulations in less time, and therefore get results quicker, learn quicker, publish quicker, graduate quicker, etc.
While some common algorithms have been optimized, not every algorithm has, and perhaps for your problem/algorithm this is an area of research.
  However, many of the same techniques can be employed for various algorithms.
Matrix Size | myDGEMM | OpenBLAS | MKL
100 | 0.001 | 0.064 | 0.002
500 | 0.068 | 0.069 | 0.007
1000 | 0.559 | 0.291 | 0.034
2000 | 6.160 | 0.749 | 0.231
4000 | 50.341 | 2.822 | 1.682
30x!

## Slide 6: What is performance?
What does it mean for a code to be fast?
The real metric: Time
Do things efficiently in time
Derived metrics
  FLOPS = FLoating Point OPerations per Second
  Bandwidth = data per unit time (sort of like a flow rate)
  Latency = Minimum time for data to travel from point A to point B
Theoretical Peak Performance
  Very difficult to achieve in practice
  Can be computed from hardware specs
Good serial metric: % of theoretical peak
  ...maybe
How do you get fast code?
First: Choose the right algorithm
Second: Understand how to express that algorithm optimally in the programming language
Third: Understand how the source code will get mapped to the hardware
Fourth: Tune the code to the hardware
A lot of this can be done with pen and paper

## Slide 7: Things to keep in mind about architecture
FPU
ALU
Processor
Data Cache
Instr. Cache
L2 Cache
Main Memory
… levels of cache
Registers
 | Register | L1 | L2 | L3 | DRAM | Cluster | Disk | Tape
Size | < 1 KB | ~1KB | 1 MB | 10’s MB | 1-100’s GB | TB | TB | PB
Speed | < 1ns | <1 ns | ~1 ns | 1-10 ns | 20-100ns | 1-100 μs | 10 ms | ~10s
“Typical” Memory Hierarchy Access Times (circa 2015)
L1 Cache

## Slide 8: Peak Performance
Example: Intel Haswell
  What is the maximum FLOPs per cycle?
    Need to look at SIMD information on processor
    If we have AVX it supports a 256-bit vector so it can operate on 4 doubles
  Does it support a fused multiply add (FMA instruction)?
    Yes, so the chip can execute 4 FMA instructions (8 FLOPs) at once
  How many vector units does it have?
    Apparently it has 2 vector units… so now we’re at 16 FLOPs at once
  How many cycles to execute an FMA instruction (which is two operations)?
    Not always easy to find… common to assume 1 cycle.
      However there may be other limiting factors such as latency (5 cycles in this case)
  What is the clock speed (cycles per second)? 2.50 GHz
    Well with AVX it appears to be 2.1 GHz
  How many cores does it have? 12
16 FLOPs/cycle × 2.5e9 cycles/second × 12 cores = 480 GFLOPS
  16 FLOPs ÷ 5 cycle × 2.1e9 cycles/second × 12 cores = 80 GFLOPS
Another derived metric is fraction of theoretical peak
Two Lessons from this:
This should be an easy calculation
Finding the right information can get quite complicated
Best to provide references e.g. document or presentation from the manufacturer

## Slide 9: Algorithm Performance
Not all algorithms are created equally
  e.g. Big-O notation O(n2) vs O(n log n)
Not all implementations (algorithms really) are created equally
  Can have “same” implementations with vastly different performance
Very few algorithms allow you to achieve sustained performance at a significant fraction of the theoretical peak
Let’s go through an example

## Slide 10: Simple Performance Model
Assume just 2 levels of memory in hierarchy: fast memory and slow memory
Consider a model to predict execution time for some set of operations
Minimum possible time is FtF when all data is in fast memory
Can also rewrite as
F= # of FLOPs
L=# of loads
tF = time for flop
tM= time for memory load/store
T = execution time
tM/tF is machine balance  key to machine efficiency
Generally tF << tM
F/L=q is computational efficiency  key to algorithm efficiency
Larger q means time is closer to minimum.
q ≥ tM / tF to get at least half of the peak speed!

## Slide 11: Matrix-Vector Multiply
{implements y = y + A*x}
for i = 1:n
for j = 1:n
y(i) = y(i) + A(i,j)*x(j)

## Slide 12: Analysis of Matrix-Vector Multiply
Assume all data for variables starts in slow memory
  L = number of slow memory loads & stores
  F = number of arithmetic operations
  q =
{read x(1:n) into fast memory}
{read y(1:n) into fast memory}
for i = 1:n
{read row i of A into fast memory}
for j = 1:n
y(i) = y(i) + A(i,j)*x(j)
{write y(1:n) back to slow memory}
Notes: L = n^2 + 3n
F = 2n^2
q = 2

## Slide 13: Plug-n-Chug
Some real data
  From Flux tM =8 ns (assuming L3 access time) and assume tF = 0.3 ns (1 cycle)
Table B.1 and B.2 from R. Vuduc Dissertation: http://bebop.cs.berkeley.edu/pubs/vuduc2003-dissertation.pdf
machine balance
(q must be at least
this for ½ peak speed)

## Slide 14: Simplifying Assumptions
Lets make sure we’re aware of the simplifying assumptions in this model and analysis
  Ignored parallelism in processor between memory and arithmetic within the processor
    Sometimes drop arithmetic term in this type of analysis
  Assumed fast memory was large enough to hold three vectors
    Reasonable if we are talking about any level of cache
    Not if we are talking about registers (~32 words)
  Assumed the cost of a fast memory access is 0
    Reasonable if we are talking about registers
    Not necessarily if we are talking about cache (e.g. 1 or 2 cycles for L1)
  Memory latency is constant
So this analysis still assumes a “best case” scenario

## Slide 15: Other Performance Models
Latency based execution time model for “Single Processor”
Most generally when dealing with complex kernels
F= # of FLOPs
L=# of loads
α = cache access latency
M = cache misses
T = execution time
Ni = Number of operations of type i
ti = time to execute operation of type i

## Slide 16: Roofline Models
Visual representation of performance relating arithmetic intensity (q) and hardware performance limits

## Slide 17: Optimization

## Slide 18: Things people say about Optimization
"We should forget about small efficiencies, say about 97% of the time: premature optimization is the root of all evil. Yet we should not pass up our opportunities in that critical 3%. A good programmer will not be lulled into complacency by such reasoning, he will be wise to look carefully at the critical code; but only after that code has been identified"
  Donald Knuth
“You’re bound to be unhappy if you optimize everything”
  Donald Knuth
“The best optimization you will ever have is to have your program go from not working to working”
  paraphrasing

## Slide 19: How Optimization Should Look (Profiling)
Kernel or Solver (~10%)
Rest of code (~90%)
Lines of Code
Contribution to Execution Time
Kernel or Solver (~90%)
Rest of code (~10%)

## Slide 20: Common Optimization Techniques
Before you program
  Choose the best algorithm
    e.g. choose known fastest converging algorithms or algorithms with asymptotically small operation counts
  Choose the best way to express this algorithm in a programming language
    Perform algebra to minimize operations or minimize memory traffic and communication
    Design data structures around computational kernels & maximize cache locality
As you are programming
  compiler optimization flags
  choose best operators (remove unnecessary FLOPs)
  loop unrolling (pipelining & vectorization)
  remove conditionals (lets compiler optimize loops better)
  function tabulation (remove unnecessary FLOPs)

## Slide 21: Compiler flags
GCC compiler option | Meaning
-O0 | Reduce compilation time and make debugging produce the expected results. This is the default.
-O1 | compiler tries to reduce code size and execution time, without performing any optimizations that take a great deal of compilation time. (favors size of executable)
-O2 | Performs nearly all supported optimizations that do not involve a space-speed tradeoff. Includes all -O1 optimizations
-O3 | Highest level of optimization. Includes all -O2 optimizations
-Ofast | Disregard strict standards compliance. -Ofast enables all -O3 optimizations. It also enables optimizations that are not valid for all standard-compliant programs.
-Og | Optimizations safe for debugging
-fipa-pta | Perform interprocedural pointer analysis and interprocedural modification and reference analysis. This option can cause excessive memory and compile-time usage on large compilation units. It is not enabled by default at any optimization level.
-funsafe-math-optimizations | Allow optimizations for floating-point arithmetic that (a) assume that arguments and results are valid and (b) may violate IEEE or ANSI standards.

## Slide 22: Operator Choice
Avoid exponentiation
  Polynomial evaluation
    e.g. Correlations for material properties, Semi-empirical models for coefficients
Division is allegedly more expensive than multiplication
t2=t**2.0 !slowest
t2=t**2 !slow
t2=t*t !fastest
DO i=1,n
a(i)=b(i)/c
ENDDO
rc=1.0d0/c
DO i=1,n
a(i)=b(i)*c
ENDDO
c=a**b
c=EXP(b*LOG(x)) !may be faster
When its unavoidable

## Slide 23: Expose Independent Operations
Hide instruction latency
  Use local variables to expose independent operations that can execute in parallel or in a pipelined fashion
  Balance the instruction mix (e.g. what functional units are available?)
f1 = f5 * f9;
f2 = f6 + f10;
f3 = f7 * f11;
f4 = f8 + f12;

## Slide 24: Exploit Multiple Registers
Reduce demands on memory bandwidth by pre-loading into local variables
while( … ) {
*res++ = filter[0]*signal[0]
+ filter[1]*signal[1]
+ filter[2]*signal[2];
signal++;
}
float f0 = filter[0];
float f1 = filter[1];
float f2 = filter[2];
while( … ) {
*res++ = f0*signal[0]
+ f1*signal[1]
+ f2*signal[2];
signal++;
}
also: register float f0 = …;

## Slide 25: Loop Unrolling
Compilers are not necessarily very good (or not as good as we’d like sometimes) at interpreting how to optimize loops
  So compilers will do this if right flags are provided and loops are “clear” enough to compiler
subroutine lngth1(n,a,s)
integer :: n
real(8) :: s,a(n)
integer :: i
s=0.d0
do i=1,n
s=s+a(i)*a(i)
enddo
endsubroutine
!works correctly only if the array size is a multiple of 4
subroutine lngth4(n,a,s)
integer :: n
real(8) :: s,a(n)
integer :: i
real(8) :: t1,t2,t3,t4
t1=0.d0; t2=0.d0; t3=0.d0; t4=0.d0
do i=1,n-3,4
t1=t1+a(i)*a(i)
t2=t2+a(i+1)*a(i+1)
t3=t3+a(i+2)*a(i+2)
t4=t4+a(i+3)*a(i+3)
enddo
s=t1+t2+t3+t4
endsubroutine
Unrolled to a depth of 4

## Slide 26: Loop Unrolling (2)
Exploits vector instructions and pipelining
Cannot be done to arbitrary size
  Registers will get overloaded
  Size should be “register-blocked” or “cache-blocked”.
subroutine lngth4(n,a,s)
integer :: n
real(8) :: s,a(n)
integer :: i
real(8) :: t1,t2,t3,t4,tr
t1=0.d0; t2=0.d0; t3=0.d0; t4=0.d0; tr=0.d0
do i=1,n-3,4
t1=t1+a(i)*a(i)
t2=t2+a(i+1)*a(i+1)
t3=t3+a(i+2)*a(i+2)
t4=t4+a(i+3)*a(i+3)
enddo
do j=n-MOD(n,4)+1,n
tr=tr+a(j)*a(j) !in practice need “remainder”
enddo
s=t1+t2+t3+t4+tr
endsubroutine

## Slide 27: Remove conditionals from loops
Loops that have branching constructs are usually not optimized by compiler
  Set all even indices to 0 and all odd indices to 1
DO i=1,SIZE(a)
IF(MOD(i,2 == 1)) THEN
a(i)=1
ELSE
a(i)=0
ENDIF
ENDDO
DO i=1,SIZE(a),2
a(i)=1
ENDDO
DO i=2,SIZE(a),2
a(i)=0
ENDDO
DO i=1,SIZE(a)-1,2
a(i)=1
a(i+1)=0
ENDDO
IF(MOD(SIZE(a),2) == 1) &
a(SIZE(a))=1

## Slide 28: Removing False Dependencies
Using local variables, reorder operations to remove false dependencies
With some compilers, you can declare a and b unaliased.
  Done via “restrict pointers”, compiler flag, or pragma.
a[i] = b[i] + c;
a[i+1] = b[i+1] * d;
float f1 = b[i];
float f2 = b[i+1];
a[i] = f1 + c;
a[i+1] = f2 * d;
false read-after-write hazard
between a[i] and b[i+1]

## Slide 29: Function tabulation
Some special functions (exponential, logarithm, gamma function, error function, etc.)
  Require many FLOPs to evaluate to double precision.
Tabulate function and linearly interpolate result
  Introduces interpolation error.
  Error is generally proportional to of table size
  If evaluating the table A LOT, want table to be small enough to fit into cache
In some cases, we can accept interpolation error because we do not know physical value to double precision (e.g. 15 digits) accuracy.

## Slide 30: More advanced techniques
Memory blocking
Cache oblivious ordering
Communication Avoiding Algorithms (State of the Art)
{implements C = C + A*B}
for i = 1 to n
{read row i of A into fast memory}
for j = 1 to n
{read C(i,j) into fast memory}
{read column j of B into fast memory}
for k = 1 to n
C(i,j) = C(i,j) + A(i,k) * B(k,j)
{write C(i,j) back to slow memory}
Naïve Matrix Multiply
=
+
*
C(i,j)
A(i,:)
B(:,j)
C(i,j)
Algorithm has 2*n3 = O(n3) Flops and operates on 3*n2 words of memory
q potentially as large as 2*n3 / 3*n2 = O(n)

## Slide 31: Memory Blocking (Tiling)
Idea: improve computational intensity and temporal locality of data.
Consider A,B,C to be N-by-N matrices of b-by-b subblocks where b=n / N is called the block size
for i = 1 to N
for j = 1 to N
{read block C(i,j) into fast memory}
for k = 1 to N
{read block A(i,k) into fast memory}
{read block B(k,j) into fast memory}
C(i,j) = C(i,j) + A(i,k) * B(k,j) {do a matrix multiply on blocks}
{write block C(i,j) back to slow memory}
=
+
*
C(i,j)
C(i,j)
A(i,k)
B(k,j)

## Slide 32: Analysis of Blocked Matrix Multiply
Recall:
  m is amount memory traffic between slow and fast memory
  matrix has nxn elements, and NxN blocks each of size bxb
  f is number of floating point operations, 2n3 for this problem
  q = f / m is our measure of algorithm efficiency in the memory system
So
m = N*n2 read each block of B N3 times (N3 * b2 = N3 * (n/N)2 = N*n2)
+ N*n2 read each block of A N3 times
+ 2n2 read and write each block of C once
= (2N + 2) * n2
So computational intensity q = f / m = 2n3 / ((2N + 2) * n2)
 n / N = b for large n
So we can improve performance by increasing the blocksize b
Can be much faster than matrix-vector multiply (q=2)
Larger block size = more efficient
Limit: All three blocks from A,B,C must fit into fast memory
Assume fast memory size Mfast
3b2  Mfast, so q  b  (Mfast/3)1/2

## Slide 33: Cache Oblivious Algorithms
Typically implemented as recursive algorithms and recursive data structures
Tiled algorithm requires finding good block size (will depend on hardware)
Cache Oblivious Algorithms offer an alternative
  Idea is to order things in memory to minimize latency with multiple levels of memory hierarchy.
  Make use of Space Filling Curves
Advantages:
the recursive layout works well for any cache size
Disadvantages:
The index calculations to find A[i,j] are expensive
Implementations switch to column-major for small sizes
Z-Order Space Filling Curve

## Slide 34: Summary of Serial Optimizations
Details of machine are important for performance
  Processor and memory system (not just parallelism)
  What to expect? Use understanding of hardware limits
Machines have memory hierarchies
  100s of cycles to read from DRAM (main memory)
  Caches are fast (small) memory that optimize average case
There is parallelism hidden within processors
  Pipelining, SIMD, etc
Data locality is at least as important as computation
  Temporal: re-use of data recently used
  Spatial: using data nearby that recently used
Can rearrange code/data to improve locality
  Goal: minimize communication = data movement
Performance intensive code should be written clearly for compiler (not for humans)