## Slide 1: Lecture 18 Heterogeneous Architectures
Prof. Brendan Kochunas
11/06/2019
NERS 590-004

## Slide 2: Outline
Introduction
GPU Architecture
Programming GPUs
  CUDA
  Others
  Kokkos

## Slide 3: Motivation
Hardware limits of serial performance
  Moore’s law no longer holds
Performance gain is now often gained through parallelism
GPUs offer massive parallelism
Required to use GPUs on some modern HPC clusters!

## Slide 4: Learning Objectives
Basic knowledge of GPU architecture
Knowledge of how to program for GPUs
  CUDA, Kokkos
  What is important for efficiency?
    Memory Layout
    Thread Scheduling
  Portability

## Slide 5: What is a GPU? Why do we care?
Graphics Processing Unit
  As the name suggests, historically used for processing graphics
  Card in computer (PCI/PCIe)
  Unified shader pipeline – different “shaders” used in graphics processing
    All shaders require: texturing (data loads), math operations (FLOPs)
    Unified pipeline allows for better GPU utilization
  Data loads + math operations? Sounds a lot like normal computing?
GPGPU – General Purpose GPU
  GPUs unified shader pipeline allows for us to use them in general computing!

## Slide 6: Why use a GPU?
GPUs have a lot of small cores
  Opportunity for massive parallelism
  But… threads are executed in SIMD within warps! (Data parallelism)
CPU is “low latency, low throughput”
  Serial and moderate parallel calculations
GPU is “high latency, high throughput” → streaming processor
  i.e. good for most highly parallel applications (think simulations)

## Slide 7: GPU Architecture
Notes: - Make diagram using lstopo – add GPU (slide 1)

## Slide 8: lstopo
CPU shown on the left (NUMA node)
  See each core, cache-level
GPU is shown as a PCI device (right)
https://www.google.com/search?q=image+of+gpu&source=lnms&tbm=isch&sa=X&ved=0ahUKEwixsvnYnMDeAhUE0oMKHSXXC7IQ_AUIEygB&biw=1368&bih=722#imgrc=J4rnsk1P30xTOM:

## Slide 9: Heterogeneous System Architectures
Serial code sections
  Few applications are completely parallel
Amdahl’s law:
  p is the proportion of the program that can be parallelized
  s is the speedup of that parallelization
Read Input
Setup
Parallel Computation
Serial Computation
Output
Visualization
CPU
GPU

## Slide 10: GPU Architecture
A modern GPU has several Streaming Multiprocessors (SMs)
  Pascal SM - 64 CUDA cores
  Tesla GP100 – 56 SMs
  Totally: 3584 CUDA cores
Each SM has “warps” (2)
  Each warp performs operations in SIMT fashion
    Single Instruction Multiple Thread
https://devblogs.nvidia.com/inside-pascal/

## Slide 11: CPU vs GPU
CPUs
Designed for Task Parallelism:
  Each thread executes a task
  Tasks have different instructions
  Relatively low number of threads
  Within core/thread SIMD (4)
Large cache to hide latency
Only option for serial applications
GPUs
Data Parallelism:
  SIMT model (SIMD)
  Same instruction on different data
  Large number of threads (10,000+)
Stream Processing:
  Large set of data (stream)
  Run same series of operations on all the data
    Series of operations is called a kernel

## Slide 12: CUDA

## Slide 13: CUDA
CUDA is a platform and API for utilizing GPUs
  C/C++ and Fortran
  Only works for Nvidia GPUs!
  Host = CPU
  Device = GPU
Memory management
  Host vs device memory
  Explicit data passing
  Unified memory (CUDA 6+)
https://devblogs.nvidia.com/unified-memory-in-cuda-6/
Notes: Models for controlling what hardware your data is on
Connection to MPI

## Slide 14: Basics – Kernels
Kernel
  Essentially a function to be performed on the device (GPU)
  Use __global__ keyword to indicate device code
  Call with
__global__ void mykernel(…);
<<<gridDim, blockDim>>>mykernel(...);

## Slide 15: Basics – Threads, Blocks, Grids
Threads are organized into a grid of blocks
  A grid is a collection of blocks – Executed on a single GPU
  A block is a collection of threads – Executed on a single SM
  A thread is the smallest unit – Executed on a single scalar core
A thread represents a single scalar core performing work
  Threads are grouped into “warps” (32 threads) – SIMT
Indexing can be multidimensional
<<<gridDim, blockDim>>>mykernel(...);

## Slide 16: Basics – Indexing/Parallelism
Within a kernel
  the grid and block sizes are available: gridDim.x, blockDim.x
  the block and thread indices are available: blockIdx.x, threadIdx.x
  Calculate global index from these
  Multidimensional indexing → replace x with y,z!
What is the point of having blocks and threads?
  Threads can communicate/synchronize!
  Shared memory

## Slide 17: Let’s do an example…
Matrix-matrix multiplication
  C = AB
Naïve approach
Each element in C is given by
  Dot product of corresponding row and column in A and B, respectively
A
C
B

## Slide 18: Matrix-matrix multiplication (1)
To make memory access patterns more obvious – flatten arrays
7
8
6
0
1
2
4
5
3
Why are memory access patterns important?
  Threads (cores) are grouped in warps
  Warps operate in SIMT fashion (lock-step)
  If 1 has a cache-miss all have a cache-miss (effectively)
Linear memory accesses
  A, C should be row-major
  B should be column-major

## Slide 19: Matrix-matrix Multiplication (2)
On CPU – Naïve matmul
  Loop through elements in C
    Loop over corresponding row/column in A/B
Matrices have been flattened
  A, C = Row-Major
  B = Column-Major
void matmul(unsigned n, unsigned m, unsigned p, double* A, double* B, double* C){
unsigned A_idx = 0; unsigned B_idx = 0; unsigned C_idx = 0;
for(unsigned row = 0; row < n; ++row){
for(unsigned col = 0; col < p; ++col) {
// Compute element of C at (row, col)
A_idx = row * m; B_idx = col * m;
// Initialize to zero
C[C_idx] = 0.0f;
// Loop over row/col of A/B (respectively)
for(unsigned idx = 0; idx < m; ++idx){
// Summation for the element
C[C_idx] += A[A_idx] * B[B_idx];
// Increment indices in A, B
++A_idx; ++B_idx;
}
// Increment the global C index
++C_idx;
}
}
}

## Slide 20: Matrix-matrix Multiplication (3) - Threads
On GPU
  Parallelize w/ threads
  Hardware limits number of threads
Not general
Not fast
__global__ void matmul(unsigned n, unsigned m, unsigned p, double* A, double* B, double* C){
// Each thread gets an INDEPENDENT element of C
// From the index...we compute row and column
unsigned C_idx = threadIdx.x;
unsigned row = C_idx / p;
unsigned col = C_idx - p * row;
// Then compute A, B indices (starting)
unsigned A_idx = m * row;
unsigned B_idx = m * col;
// Initialize to zero
C[C_idx] = 0.0f;
// Loop over row/col of A/B (respectively)
for(unsigned idx = 0; idx < m; ++idx){
// Summation for the element
C[C_idx] += A[A_idx] * B[B_idx];
// Increment indices in A, B
++A_idx; ++B_idx;
}
}

## Slide 21: Matrix-matrix Multiplication (4) - Blocks
On GPU
  Parallelize w/ blocks of threads
  General
  Not very fast though
Memory accesses
  Each thread has a single element of C
  Each thread accesses contiguous chunks of A, B
  Very small cache
    Reloading A, B values!
__global__ void matmul(unsigned n, unsigned m, unsigned p, double* A, double* B, double* C){
// Each thread gets an INDEPENDENT element of C
// From the index...we compute row and column
unsigned C_idx = blockDim.x * blockIdx.x + threadIdx.x;
unsigned row = C_idx / p; unsigned col = C_idx - p * row;
// Then compute A, B indices (starting)
unsigned A_idx = m * row; unsigned B_idx = m * col;
// Initialize to zero
C[C_idx] = 0.0f;
// Loop over row/col of A/B (respectively)
for(unsigned idx = 0; idx < m; ++idx){
// Summation for the element
C[C_idx] += A[A_idx] * B[B_idx];
// Increment indices in A, B
++A_idx; ++B_idx;
}
}

## Slide 22: Matrix-matrix Multiplication (5) - Tiling
On CPU
  Tiling increases cache locality → fewer misses
On GPU
  Tiling increases cache locality → fewer misses
  A, B tiles (submatrices) can be loaded into shared memory (cache)
    Fewer loads, fewer misses
    Relatively small tiles → fits in cache!
  Significantly better performance!

## Slide 23: Summary of Cuda
Control
  Over where data is stored
  Over where functions are executed
Kernels are executed on GPU
  Kernel functions marked by keyword __global__
Parallelism is hierarchical
  Grid of Blocks of Threads
  A block of threads should work on contiguous memory
  A single thread should move through memory with stride-1 access

## Slide 24: Other Approaches for GPGPUs

## Slide 25: OpenCL
What is OpenCL?
  Programming framework for heterogeneous systems
    Includes CPUs, GPUs, DSPs, FPGAs, etc
  Maintained by Khronos Group
Portability
  …at what cost?
https://en.wikipedia.org/wiki/OpenCL

## Slide 26: OpenCL – Execution Model
Abstract Execution Model
  Work Item – Basic unit of work on compute device (GPU)
  Kernel – Code that runs on a work item
  Program – Collection of kernels and other functions
  Context – Environment where work items execute
  Command Queue – Queue used by host to submit work to the device(s)
Work size
  Global work size, work-group size
  Effectively same as grids, blocks in CUDA

## Slide 27: CUDA and OpenCL
https://leonardoaraujosantos.gitbooks.io/opencl/chapter1.html

## Slide 28: OpenMP(4+) and OpenACC
OpenMP and OpenACC
  Offer directive based approach for writing GPU code
Typically simpler than writing CUDA/OpenCL codes
  Typically worse performance
  ...Compilers are making progress
Portability
  At what cost?
Notes: OpenACC absorption
Compiler optimization is improving

## Slide 29: Portability?
Is portability a good thing?
Code may be portable…but not efficient!
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
CPU
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
GPU

## Slide 30
“You cannot make a solution independent of the actual platform or finite set of platforms. Reality is not a hack you’re forced to deal with to solve your abstract, theoretical problem. Reality is the actual problem.”
– Mike Acton, CppCon 2014 “Data-Oriented Design and C++” https://www.youtube.com/watch?v=rX0ItVEVjHc

## Slide 31: Another look
0
1
2
3
0
1
2
3
0
1
2
3
0
1
2
3
0
1
2
3
CPU
0
0
0
0
1
1
1
1
2
2
2
2
3
3
3
3
GPU
0
0
0
0
0
1
2
3
CPU w/ SIMD
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 32: CPU and GPU Programming
Threads on GPUs are (somewhat) analogous to Instruction Level Parallelism (ILP) on CPU
Blocks on GPUs are (somewhat) similar to threads on CPUs
  No communication though
Portability may be possible, but we must be aware of architecture differences!

## Slide 33: Kokkos
Open Source – Developed by Sandia National Laboratories
  https://github.com/kokkos
  Detailed training slides at https://github.com/kokkos/kokkos-tutorials
Kokkos offers performant portable code
Aims for simplicity
  Shouldn’t be more difficult than OpenMP!
  (You need some modern C++ knowledge though)
It’s a library
A lot to cover. We will see examples on Friday!

## Slide 34: Kokkos – Introduction (1)
https://github.com/kokkos/kokkos-tutorials/blob/master/Intro-Full/Slides/KokkosTutorial_ORNL18.pdf
  Pattern – structure for computations
  Policy – Range, schedule, thread teams, etc.
  Body – Work to be done (kernel)

## Slide 35: Kokkos – Introduction (2)
For performance, memory access patterns must be architecture dependent!
The Kokkos library maps work to cores
  Provide Kokkos with range and body
  Kokkos will map indices to cores (may be on GPU!)
If Kokkos is a library…how do we provide a body?
  Functors! (function with data)

## Slide 36: Kokkos – Functors
Parallel functor must have access to the data it needs through the functor’s data members
Functors are simply structs
  with void operator()(const size_t index) {…};
Or, lambdas (C++11)
  Lambdas auto-generate a functor
  Tends to be less tedious (more productivity)
Notes: Functors are function objects—operation with some data
Lambdas are anonymous functions—e.g. they’re not declared with a symbol name
Lambdas are like really really lightweight functions.
[capture](parameters) -> return_type { function_body }

## Slide 37: Functor vs Lambda Example
Functor
Lambda

## Slide 38: Kokkos – Comparison
Not more difficult than OpenMP, in concept

## Slide 39: Kokkos – Views
Views allow us to store/communicate data between host and device
  They are like pointers (you should copy, not reference)
  Templated – on data type
    And others!
    Memory Space, Layout, Memory Traits, etc. (more details to come)
  Multidimensional
    Ease of use
    Rectangular (not jagged)
  No hidden allocations! (important for performance)

## Slide 40: Kokkos – Execution Space
Execution Space tells us where the code will run
  Serial, Threads, OpenMP, Cuda, etc.
Can control via default Execution Space – Compile Time
Can specify Execution Space in the policy
  A template parameter
Need to mark non-CPU space lambda/functors with macro
  #define KOKKOS_INLINE_FUNCTION inline __device__ __host__

## Slide 41: Kokkos – Memory Space
Memory Space tells us where the data is stored
Template parameter on Views
  HostSpace, CudaSpace, CudaUVMSpace, etc.
Each Execution Space has a default memory space
If in CudaSpace
  Data is stored on GPU
  Metadata is also stored on CPU
Mirror/deep_copy

## Slide 42: Kokkos – Layouts
Multidimensional arrays in C/Fortran have different “Layouts”
  Row-major is good in some places
  Column-major is good in some places
Kokkos gives a simple approach to multidimensional array layout:
  Layout is a templated parameter on a View
  LayoutLeft → Left-most index is stride 1
  LayoutRight → Right-most index is stride 1
  More, and you can create your own

## Slide 43: Kokkos – Scheduling
On the CPU we wanted each thread to work over a contiguous chunk of memory
On the GPU we wanted each thread block to work over a contiguous chunk of memory (thread indexing strided)
Kokkos maps indices to cores in contiguous chunks on CPU and strided for GPU
Using this knowledge in addition to Layouts
  We can achieve performant portable code
  …if we choose the right layout for the architecture

## Slide 44: Kokkos – Subviews and Multiloop Parallelism
Subview
  Like a “slice” of a View
  Uses colon notation from Fortran, Matlab, Python, etc.
  No allocation occurs in construction! – but not free!
    Avoid usage if not accessing a lot
MDRangePolicy
  MultiDimensional Range Policy
  Parallelism over multiple loop levels
  Similar to collapse in OpenMP
Notes: Check openMP keyword for MDRangePolicies

## Slide 45: Kokkos – Hierarchical Parallelism
Hierarchical Parallelism allows for nested parallelism
  League of Teams of Threads vs Grid of Blocks of Threads
  Thread teams – Threads that work concurrently and can synchronize
    Think block in Cuda
    Functor/lambda operations get a team member
      teamMember.league_rank();
      teamMember.team_rank();
      blockIdx, threadIdx in Cuda
  Vector level parallelism
    Vectorizable loops on CPU
    (Sub-)warp level parallelism on GPUs

## Slide 46: Matrix-matrix multiplication
Parallel implementation of naïve matrix-matrix multiplication
  mat_l, mat_r are aliases for Kokkos::View<double**>
    LayoutLeft, LayoutRight
void matmul(unsigned n, unsigned m, unsigned p, mat_r A, mat_l B, mat_r C)
{
typedef Kokkos::MDRangePolicy< Kokkos::Rank<2> > mdrange_policy;
Kokkos::parallel_for("matmul", mdrange_policy({0, 0} , {n, p}),
KOKKOS_LAMBDA (unsigned row, unsigned col) {
for(unsigned idx = 0; idx < m; ++idx){
C(row, col) += ( A(row, idx) * B(idx, col) );
}
}
);
}

## Slide 47: Kokkos – Atomics/MemoryTraits
Atomics – Atomic Operations
  Solution to multiple threads trying to write to same location
  Locks are not scalable to 10,000+ threads
  Data replication is not scalable to 10,000+ threads
  Example: Kokkos::atomic_add(…);
Memory Traits
  Template parameter on Views
  Atomic, Read, Write, ReadWrite, ReadOnce, Contiguous, RandomAccess
  Tells compiler/Kokkos what you will do with the memory

## Slide 48: Kokkos – Scratch Space
Scratch space offers (roughly) a programmer managed cache
GPUs have small dedicated scratch space
  Kokkos lets you use these much more easily than Cuda
CPUs don’t have special hardware for this
  But, memory access patterns are cache-aware
Accessing data in this scratch space is much faster than in main memory
  Level 0 fastest
  Level 1 fast

## Slide 49: Kokkos – Summary
Offers Portability
  without compromising performance
Simple things are just as simple as in OpenMP
Advanced tuning is simpler than native implementations
  For GPUs
  Not so much for CPUs

## Slide 50: Useful resources
https://devblogs.nvidia.com
  https://devblogs.nvidia.com/even-easier-introduction-cuda/
  https://devblogs.nvidia.com/unified-memory-cuda-beginners/
  https://devblogs.nvidia.com/inside-pascal/
http://www.cs.cmu.edu/afs/cs/academic/class/15668-s11/www/cuda-doc/CUDA_C_Programming_Guide.pdf
https://github.com/kokkos/kokkos-tutorials